## Slide 1: HIGH FREQUENCY LONGITUDINAL SURVEYS OF THINGS: Real Time Energy Monitoring IN Tajikistan
Joao Pedro Azevedo and William H. Seitz
In collaboration with Dana Rysankova, Elisa Portale, and Gouthami Padam (esmap global team) and Arthur Kochnakyan and Takhmina Mukhamedova (Tajikistan energy team)
Leveraging Open, Big and Geospatial Data Innovations within EEX Operations
March 2017

## Slide 2: Satellite Sensor Details
NOAA Visible Infrared Imaging Radiometer Suite (VIIRS) onboard the Suomi National Polar-Orbiting Partnership (Suomi NPP)
Sensor
Day/Night Band (DNB)
5 High resolution Imagery channels (I-bands)
16 Moderate resolution channels (M-bands)
Available bands
Using this band

## Slide 3: Metadata of available imagery
Most images taken around 9pm!!!
A total of 317 daily images from October 1, 2016 to April 30, 2017

## Slide 4
Sample night image

## Slide 5: Why do we need ground truth data?
This was a high scale power outage on October 28, 2016.

## Slide 6: Ground sensors easily captured the nation-wide outage
Only 5 out of the 150 locations had power on October 28, between 8-9pm

## Slide 7: Can we easily differentiate using imagery?
Day (2016-10-28 21:00:00) with massive power outage, only 3 locations had power
Regular day (2017-02-26 20:00:00), 104 monitoring locations had power at this hour

## Slide 8: Night images vs. actual power failure data: explore correlation
The key question is to determine how well the night images (radiance values) can match what's happening on the ground (power status from our box data)
Visual exploration
Predict power status in our box data using image

## Slide 9: Preprocessing the data for this analysis
Dataset used for this analysis
Images matched to box events by the hour (image capture date truncated to hour precision)
For boxes, only considered hours which had same same events from the two boxes in the same psu (just being strict)
Extract pixel values at the psu location given by longitude, latitude.

## Slide 10: Very visible correlation between images and actual state of power
Clear separation of trends when power is on vs when power if off
Use log (radiance) instead of actual radiance

## Slide 11: Can raw pixel values predict hourly power status?
All test models perform better than baseline